## Slide 1: REFUGEE HOUSING UNIT RESEARCH AND DEVELOPMENT PROJECT
Notes: A 15min presentation of the Refugee Housing Unit – an angoing design and development project of UNHCR, IKEA Foundation and RHU.

## Slide 2: SCOPE
To develop an emergency to semi permanent shelter solution which significantly improve the lies of refugees and internally displaced people.
Notes: ¨SCOPE statement,
Add hand drawn skteshes-

## Slide 3
Usability
Safety
Helath and comfort
Deplyment
Environmemt and code of conduct
Deployment
Cost effective
KEY REQUIREMENT AREAS:
Notes: A very brief overview – detail questions to be discuessed after presentation.
Usability: Lifespan 3yrs panels, 10 years for frame. Modular, 17,5m2/5people Return time and user time depending on local situation.
Safety: Structural integrity of wind = 16,8m/23m/s, snow load of 50mm (175kg), Solar load, 3 years Kenya.
Health and comfort, moitsure, Infiltration, Ventilation, etc. Calculated and beeing tested to verify
Deploymnet: Flat packed. Volume 1 cbm. Weight 120kg without shade net. Target weight 100 kg. Easy and quick to install/maintain.
Cost effective: Reasonable up-front cost, low lifecycle cost.

## Slide 4
THE RHU FRAME
Notes: THE RHU FRAME is a modular and expandable self-supported frame designed to be used with RHU Panels, plastic sheeting or locally sourced building materials in order to build an adequate shelter. To date only tested with RHU panels.

## Slide 5
THE RHU PANELS
Notes: THE RHU PANELS are modular wall and ceiling panels to be built on to the RHU Frame in order to quickly achieve a complete, durable shelter intended to last minimum three years. The Panels can be fitted onto a RHU Frame in any size

## Slide 6
THE RHU SHADE NET
Notes: THE RHU SHADE NET is an external screen, which significantly improves indoor thermal comfort. During the day, the Shade Net´s open structure provides 70% solar reflection and cooling. At night and in cold climates, the Shade Net helps reduce radiated heat loss.

## Slide 7
THE RHU PV SYSTEM
Notes: THE RHU PHOTOVOLTAIC (PV) SYSTEM consists of a solar panel and a portable LED light including battery and USB power output. The solar panel can be integrated into the RHU Panel or the RHU Shade Net.
3w/330 lumens, € hrs use at max, 12 hours at min, USB out to chareg cellpohones etc.

## Slide 8
REFUGEE HOUSING UNIT PILOT DOLLO ADO, ETHIOPIA
Notes: Pilot on Dollo Ado, Ethiopia. Somali refugee camps Hilwayen and Kobe.
Tested full supply chain, manufacturing, storage and logistics handling training, deplymnet and use.

## Slide 9
Notes: RHU in warehouse Sweden

## Slide 10
Notes: Same RHU Pacakges after transport to Dollo…

## Slide 11
Notes: Training – ground assembly

## Slide 12
Notes: Training - Paneling

## Slide 13
Notes: Training - Roof and walls

## Slide 14
Notes: Training – First Unit complete (no shade net)

## Slide 15
Notes: Deployment – working in a seqential process (to speed up assembly). How to deploy in the field for best effeciency is subject to further study and testing .

## Slide 16
Notes: Deploymnet – final RHUs beeing assembled.

## Slide 17
Notes: RHU interior

## Slide 18
Notes: RHU ”village” after one month – kitchenettes are beeing built in garden

## Slide 19
NEXT STEP
Testing in Dohuk, Iraq start Nov 2013
Interim test Dollo Ado, Nov 2013
Final test Dollo Ado, Feb 2013
Complete specifications Feb 2013
Notes: RHU ”village” after one month – kitchenettes are beeing built in garden